## Slide 1: In the name of god

## Slide 2: Use case point traning
Producers :
Sayyed Hoosein Hosseini
Supervisor :
Dr. Mohammad reza sharbaf
Faculty of Computer Engineering, University of Isfahan
Autumn 2023

## Slide 3: definition
Use case points (ucp or ucps) is a software estimation technique used to forecast the software size for software development projects. ucp is used when the unified modeling language (uml) and rational unified process (rup) methodologies are being used for the software design and development. the concept of ucp is based on the requirements for the system being written using use cases, which is part of the uml set of modeling techniques. the software size (ucp) is calculated based on elements of the system use cases with factoring to account for technical and environmental considerations. the ucp for a project can then be used to calculate the estimated effort for a project.
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 4: example
To illustrate the process of calculating the ucp, an online shopping system will be used. the diagram below depicts the use case diagram for the system to be developed.
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 5: Unadjusted Use Case Weight (UUCW)
to calculate the uucw, the use cases must be defined and the number of transactions for each use case identified. the online shopping system use case diagram is depicting that nine use cases exist for the system. assuming 2 of these use cases are simple, 3 are average and 4 are complex, the calculation for uucw is as follows:
UUCW = (total no. of simple use cases x 5) + (total no. average use cases x 10) + (total no. complex use cases x 15)
for the online shopping system, the uucw = (2 x 5) + (3 x 10) + (4 x 15) = 100
UUCW = 100
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 6: Unadjusted Actor Weight (UAW)
To calculate the uaw, the actors must be identified. the online shopping system use case diagram is depicting five actors; one simple for the payment processing system and four complex for each of the human users actors (i.e. online customer, marketing administrator, warehouse clerk, warehouse manager.) the calculation for uaw is as follows:
UAW = (total no. of simple actors x 1) + (total no. average actors x 2) + (total no. complex actors x 3)
for the online shopping system, uaw = (1 x 1) + (0 x 2) + (4 x 3) = 13
UAW = 13
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 7: Technical Complexity Factor (TCF)
to calculate the tcf, each of the technical factors is assigned a value based on how essential the technical aspect is to the system being developed. the diagram below shows the assigned values for the online shopping system. the values are multiplied by the weighted values and the total tf is determined.
next, the tcf is calculated:
TCF = 0.6 + (tf/100)
for the online shopping system, tcf = 0.6 + (42/100) = 1.02
TCF = 1.02
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 8
Factor | Description | Weight | Assigned Value | Weight x Assigned Value
T1 | Distributed system | 2.0 | 5 | 10
T2 | Response time/performance objectives | 1.0 | 5 | 5
T3 | End-user efficiency | 1.0 | 3 | 3
T4 | Internal processing complexity | 1.0 | 2 | 2
T5 | Code reusability | 1.0 | 3 | 3
T6 | Easy to install | 0.5 | 1 | 0.5
T7 | Easy to use | 0.5 | 5 | 2.5
T8 | Portability to other platforms | 2.0 | 2 | 4
T9 | System maintenance | 1.0 | 2 | 2
T10 | Concurrent/parallel processing | 1.0 | 3 | 3
T11 | Security features | 1.0 | 5 | 5
T12 | Access for third parties | 1.0 | 1 | 1
T13 | End user training | 1.0 | 1 | 1
Total (TF): |  |  |  | 42
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 9: Environmental Complexity Factor (ECF)
To calculate the ecf, each of the environmental factors is assigned a value based on the team experience level. the diagram below shows the assigned values for the online shopping system. the values are multiplied by the weighted values and the total ef is determined.
next, the ecf is calculated:
ECF = 1.4 + (-0.03 x ef)
for the online shopping system, ECF = 1.4 + (-0.03 * 10.5) = 1.085
ECF = 1.085
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 10
Factor | Description | Weight | Assigned Value | Weight x Assigned Value
E1 | Familiarity with development process used | 1.5 | 3 | 4.5
E2 | Application experience | 0.5 | 3 | 1.5
E3 | Object-oriented experience of team | 1.0 | 2 | 2
E4 | Lead analyst capability | 0.5 | 5 | 2.5
E5 | Motivation of the team | 1.0 | 2 | 2
E6 | Stability of requirements | 2.0 | 1 | 2
E7 | Part-time staff | -1.0 | 0 | 0
E8 | Difficult programming language | -1.0 | 4 | -4
Total (EF): |  |  |  | 10.5
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 11: Use Case Points (UCP)
once the unadjusted use case weight (uucw), unadjusted actor weight (uaw), technical complexity factor (tcf) and environmental complexity factor (ecf) has been determined, the use case points (ucp) can be calculated with the following formula:
UCP = (uucw + uaw) x tcf x ecf
for the online shopping system, UCP = (100 + 13) x 1.02 x 1.085 = 125.06
UCP = 125.06
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 12
for the online shopping system, the total estimated size to develop the software is 125.06 use case points.
now that the size of the project is known, the total effort for the project can be estimated. for the online shopping system example, 28 man hours per use case point will be used.
estimated effort = ucp x hours/ucp
for the online shopping system, estimated effort = 125.06 x 28
estimated effort = 3501 hours
ITPM USE CASE POINTS TRANING PRODUCER : Sayyed Hossein Hosseini Supervisor : Dr. Mohammad Reza Sharbaf

## Slide 13: The end
Thanks for your attention